## Slide 1: ROS for Engineers – part 1 aka ros without programming

## Slide 2: Today’s Goals
Learn what ROS is about
Learn ROS core concepts
Practice with ROS commands on Ubuntu
Learn how to launch an application
Learn how to inspect a running application
Learn how to drive a mobile robot

## Slide 3: … without programming
just using existing ROS packages

## Slide 4: ROS ?
What?

## Slide 5: What is ROS?
“The Robot Operating System (ROS) is a set of software libraries and tools that help you build robot applications. From drivers to state-of-the-art algorithms, and with powerful developer tools, ROS has what you need for your next robotics project. And it's all open source.”
  ros.org

## Slide 6: History
Originally developed in 2007 at Stanford University and continued at Willow Garage
  Quigley, M., et. al. (2009). ROS: an open-source Robot Operating System. https://www.willowgarage.com/sites/default/files/icraoss09-ROS.pdf
Since 2013 it is managed by OSRF (Open Source Robotics Foundation)
  http://www.osrfoundation.org/

## Slide 7: Robot Stack
Robot Middleware
Robot Applications
Operating System Platform
Hardware Platform
Sensors
Actuators
Controller
ROS
Ubuntu

## Slide 8: ROS: Robot Operating System
Open-source, meta-operating system
  Interproces communication framework
  Debugging, Visualization, Simulation tools
  Package and Build environment
  Federated Network of Repositories
Platform and community for sharing code
  “Standing on the shoulder of giants”

## Slide 9: Ubuntu
CTRL-ALT-T to open new Terminal window

## Slide 10: Linux File system
Tree of directories, containing files
Absolute and relative paths
/
bin
etc
mnt
dev
home
ls
cp
passwd
joe
mike
src
doc
abc.txt
proc
hello.c
/home/joe/doc/abc.txt
../../mike

## Slide 11: Frequently used Linux commands
cd change directory
ls list files and subdirectories
cat print file content
gedit start tekst editor

## Slide 12: Core concepts

## Slide 13: ROS Core Concepts
Code packaging & building
  Repositories
  Packages
  Workspace
  Catkin
Computation Graph
  Nodes
  Topics
  Messages, Services
  ROS Master, Parameters
http://wiki.ros.org/ROS/Concepts

## Slide 14: Code packaging & building

## Slide 15: Repositories
2000+ packages
GitHub
http://www.ros.org/browse/list.php

## Slide 16: Stacks of Packages
Package
  Unit for organizing software in ROS
  a collection of nodes, launch files, models, etc.
Stack (Metapackage)
  a collection of packages.

## Slide 17: Installing a package/stack

## Slide 18: Installing packages
Included in Distribution (no download necessary)
  Installed in /opt/ros/<distribution_name>/…
Binary downloads (debian packages)
  sudo apt-get install ros-indigo-package-name
Source downloads
  Usually provided on github.com
  Download in your workspace and build there

## Slide 19: Workspace
catkin_ws/
src/
CMakeLists.txt
…
my_package/
package.xml CMakeLists.txt
src/
launch/
…
…
build/
devel/
install/

## Slide 20: Package
Package.xml
  Manifest: metadata about the package (e.g. dependencies).
CMakeLists.txt
  Package build information
src, scripts, launch, msg, srv, urdf, …
  Node sources, message defs, launch files, models, etc.

## Slide 21: Building packages
Catkin
  New package build system
Rosbuild
  Old package build system
catkin_make
src/
devel/
CMakeLists.txt

## Slide 22: Computation graph

## Slide 23: ROS Computation Graph

## Slide 24: Computation Graph
Network of Nodes, connected via Topics
Publish / Subscribe pattern

## Slide 25: Nodes
Node = Executable
Performs computation, e.g.
  Read a sensor
  Compute robot location
  Navigate to goal
  Drive an actuator
At a moderate Rate (< 100 Hz)
Node
Node
Node
Sensor
Actuator

## Slide 26: Challenge
Draw a Computation Graph for this situation:
  Mobile robot
    Has Real-Time Controller
    On-board Laptop running ROS, connected to Real-Time Controller
    Camera connected to Laptop
  Laptop
    Connected to robot via Wifi
    Supports Mouse control of robot
    Robot camera image displayed in window

## Slide 27: Publishing and Service invocation
Nodes can:
  Publish messages on a topic
  Subscribe to topic and receive published messages
  Invoke a Service on another Node

## Slide 28: Message
Syntax
  fieldtype1 fieldname1 fieldtype2 fieldname2 fieldtype3 fieldname3 …
geometry_msgs/Vector3 linear
float64 x
float64 y
float64 z
geometry_msgs/Vector3 angular
float64 x
float64 y
float64 z

## Slide 29: ROS Master
Master: broker (registration and lookup)
  roscore command to start it
  includes parameter server and rosout
$ROS_MASTER_URI

## Slide 30: Advertise & Subscribe
“bar”,

## Slide 31: Get & Set Parameters

## Slide 32: Running Ros software

## Slide 33: ROS Commandline Tools
Lots of commands, e.g.
  rospack, roscd, rosls, …
    ROS filesystem navigation
  rosrun
    Run one single node
  roslaunch
    Launch group of nodes (as specified in launch file)
  rosnode, rostopic, rosservice, rosmsg, rosparam
    List, set/publish, get/echo/show, call

## Slide 34: Running a ROS node
source ~/<workspace>/devel/setup.bash
  set workspace
roscore
  start the ROS Master
rosrun <package> <node_name>
  start the node (and its topics)

## Slide 35: How ROS searches packages
/opt/ros/<distribution>/…
your_workspace
rosrun <package> <node_name>

## Slide 36: parameters

## Slide 37: Parameters
YAML
Commandline parameters
Config files (.yaml)
foo:
bar:
- name: john
- value: 1234.5
{ foo: { bar: [ { name: john }, {value: 1234.5} ] } }
rostopic pub … {linear: {x: 1.0, y: 0.0, z: 0.0}, angular: {x: 0.0 ,y: 0.0, z: 0.0}}

## Slide 38: Launching a bunch of nodes

## Slide 39: Launch file
XML
  <tag attribute=“…” />
  <tag attribute=“…”> … </tag>
  <!-- comment -->
  <launch>
  <node name="talker" pkg="chat_pkg" type="talker" output="screen"/>
  <node name="listener" pkg="chat_pkg" type="listener" output="screen"/>
  </launch>

## Slide 40: Example Launch file
<launch>
<arg name="model" default="$(find robot_urdf)/robot.urdf"
<arg name="gui" default=“True" /> <param name="robot_description“ textfile="$(arg model)"/> <param name="use_gui" value="$(arg gui)"/>
<node name="joint_state_publisher"
pkg="joint_state_publisher"
type="joint_state_publisher" >
</node>
<node name="robot_state_publisher"
pkg="robot_state_publisher" type=“robot_state_publisher" />
<node name="rviz" pkg="rviz" type="rviz"/>
</launch>

## Slide 41: Launching
roslaunch <package> <launchfile_name>

## Slide 42: How to drive a mobile robot

## Slide 43: Mobile Robots

## Slide 44: DOFs of a Free Body
Any unattached body in 3D space has 6 DOFs
  3 for translation: x, y, z
  3 for rotation: roll, pitch, yaw

## Slide 45: How to drive a mobile robot
Moving: control its translation velocity
  Linear velocity in x,y,z direction [m/s]
Turning: control its rotation velocity
  Angular velocity around x,y,z axis [rad/s]
Turning while moving forward (making curves)
  All of the above

## Slide 46: Drive any Mobile Robot
A robot_node drives the robot platform
  Subscribed topic: cmd_vel
  Receives Twist messages
geometry_msgs/Twist
  Linear velocity in x,y,z direction [m/s]
    Vector3 linear
      float64 x
      float64 y
      float64 z
  Angular velocity around x,y,z axis [rad/s]
    Vector3 angular
      float64 x (Roll)
      float64 y (Pitch)
      float64 z (Yaw)
robot_node
cmd_vel
ROBOT
Twist

## Slide 47: Drive a 2-wheel Mobile Robot
Can only move in X direction and rotate around Z
  linear.y = 0
  linear.z = 0
  angular.x = 0
  angular.y = 0
See: http://wiki.ros.org/ROS/Tutorials/UnderstandingTopics

## Slide 48: Reference materials

## Slide 49: ROS Cheatsheet
http://www.clearpathrobotics.com/ros-cheat-sheet

## Slide 50: ROS Books
A Gentle Introduction to ROS
  http://www.cse.sc.edu/~jokane/agitr/
  C++ examples
ROS By Example
  http://www.lulu.com/spotlight/pirobot
  Python examples

## Slide 51: ROS Tutorials
http://www.ros.org/wiki/ROS/Tutorials
  Start here …
  C++ and Python examples