## Slide 1: ROS for Engineers – part 2 aka ros without programming

## Slide 2: Today’s Goals
Learn how to drive a mobile robot using Twist messages
Learn the concepts of Pose and Odometry
Learn how ROS keeps track of Coordinate Frames using TF
Learn how to do Mapping , Localization, and Navigation

## Slide 3: Drive a mobile robot

## Slide 4: Mobile Robots

## Slide 5: DOFs of a Free Body
Any unattached body in 3D space has 6 DOFs
  3 for translation: x, y, z
  3 for rotation: roll, pitch, yaw

## Slide 6: How to drive a mobile robot
Moving: control its translation velocity
  Linear velocity in x,y,z direction [m/s]
Turning: control its rotation velocity
  Angular velocity around x,y,z axis [rad/s]
Turning while moving forward (making curves)
  All of the above

## Slide 7: Drive any Mobile Robot
geometry_msgs/Twist
  Linear velocity in x,y,z direction [m/s]
    Vector3 linear
      float64 x
      float64 y
      float64 z
  Angular velocity around x,y,z axis [rad/s]
    Vector3 angular
      float64 x (Roll)
      float64 y (Pitch)
      float64 z (Yaw)
robot_node
cmd_vel
ROBOT
Twist

## Slide 8: Differential Drive
Each wheel is controlled by a distinct motor.
Steering by means of different motor speeds
r

v

## Slide 9: Differential Drive

## Slide 10: Differential Drive Kinematics
Left wheel angular velocity
Right wheel angular velocity
r

v
L
R
R
SUMMARY

## Slide 11: Drive a 2-wheel Mobile Robot
Robot with 2-wheel differential drive can only move in X direction and rotate around Z axis
  linear.y = 0
  linear.z = 0
  angular.x = 0
  angular.y = 0
rostopic pub -r 10 /turtle1/cmd_vel geometry_msgs/Twist "{linear: {x: 2.0}, angular: {z: 1.8}}"
rostopic pub -r 10 /turtle1/cmd_vel geometry_msgs/Twist '[2.0, 0.0, 0.0]' '[0.0, 0.0, 1.8]'

## Slide 12: odometry

## Slide 13: Pose
Robot’s posture in free space
  Position
    (x,y,z)
  Orientation
    Quaternion (x,y,z,w)
    RPY(r,p,y)
y
x
z
Z
X
Y

## Slide 14: Quaternions
Better then RPY (Euler)
  No “gimbal lock”
  Better interpolation
  Easier calculations
    http://www.gamasutra.com/view/feature/131686/rotating_objects_using_quaternions.php
ROS Refs
  http://answers.ros.org/question/9981/what-are-quaternions-and-how-can-iuse-them/
  http://answers.ros.org/question/9772/quaternions-orientationrepresentation/
https://en.wikipedia.org/wiki/Quaternion

## Slide 15: Odometry
Estimate of current Pose and Twist
  using proprioceptive sensors (e.g. wheel encoders)
  integration of distances while driving
Good for short term, relative position estimate.
Error / uncertainty grows while driving
  systematic and non-systematic errors.
http://ros.org/doc/api/nav_msgs/html/msg/Odometry.html
(0,0,..)
(x,y,…)

## Slide 16: Robot Odometry
robot_node
/odom
Odometry
http://www.youtube.com/watch?v=S4EkL68uB0c
/cmd_vel
Twist
wheel encoders
pose, velocities
velocities

## Slide 17: Enhanced Odometry
robot
_node
driver
/odom
robot _pose_ekf
/odom_combined
/imu_data
GYRO
/cmd_vel
http://www.ros.org/wiki/robot_pose_ekf
/vo
GPS
3D orientation
3D pose
2D pose
/tf

## Slide 18: TF
Where is everything?

## Slide 19: Coordinate Frames
Camera
y
z
x
World (Map)
y
x
z
Robot
Z
Y
X
y
x
z
Object

## Slide 20: Frames for Mobile Robots
http://www.ros.org/reps/rep-0105.html

## Slide 21: Frames for Mobile robots
  map
    origin: “origin of the map”
    long-term global reference
  odom
    origin: “where the odometry calculation started”
    short-term local reference
  base_link
    origin: “central point on the robot”
      rotational center of mobile base
      waist of humanoid or manipulator
    origin of robot coordinate frame

## Slide 22: Frames for Humanoids & Manipulators
http://www.ros.org/reps/rep-0120.html

## Slide 23: TF
Provides a uniform way to publish and look up transformations between coordinate frames
TF keeps track of a tree of frames
  A frame is identified by ‘frame_id’ string
  A frame has one parent, any number of child frames
  Every link in the tree represents a transform between two frames: parent and child
    Transform = pose of child in the frame of parent
http://www.ros.org/wiki/tf

## Slide 24: TF Tree

## Slide 25: TF Tree

## Slide 26: Typical Transforms & Broadcasters
map  odom
  localization/mapping nodes (e.g. amcl, gslam)
odom  base_link
  odometry nodes (e.g. robot_pose_ekf)
base_link  <other links on the robot>
  state publishing nodes (e.g. robot_state_publisher)

## Slide 27: TF Broadcasters
robot_pose_ekf
/tf
/odom
robot_state_publisher
/imu_data
/joint_states
odom  base_link
base_link  …
robot_node
amcl gmapping
/scan
map
map  odom
kinect/laser_node
robot_description

## Slide 28: Special TF Broadcasters
static_transform_publisher
  http://www.ros.org/wiki/tf#static_transform_publisher
  input via commandline arguments (manual or launch file)
  publishes one static coordinate transform to TF
robot_state_publisher
  http://www.ros.org/wiki/robot_state_publisher
  Reads parameter robot_description (URDF robot model)
  subscribes to topic /joint_states
  publishes all (static + dynamic) state of the robot to TF

## Slide 29: TF Listeners
/tf
rviz

## Slide 30: Mapping, Localization, Planning, Navigation
Where are we? How do we get there?

## Slide 31: Making the robot more intelligent
Planning & Navigation
Localization
Mapping
Control
/ tf
/odom
/cmd_vel
/goal

## Slide 32: What do we need?
A Map
Sensors to look around
A way to determine location (pose) from sensor data
A way to do path planning & navigation

## Slide 33: Probabilistic Robotics
Accept that motion, manipulation and sensing all give noisy and uncertain results
Explicitly represent uncertainty using the calculus of probability theory

## Slide 34: The Real World: Noisy Motion Data
accumulation of odometry errors
Start

## Slide 35: The Real World: Noisy Sensor Data
Noisy measurements
E.g. Measured distances for expected distance of 300 cm.
Sonar
Laser

## Slide 36: Occupancy Grid Map
Each cell: probability that it is occupied
http://www.ros.org/doc/api/nav_msgs/html/msg/OccupancyGrid.html

## Slide 37: Bayes Rule
posterior

## Slide 38: Pose Estimation
Calculate Believe of the robot about its pose x from its recorded motions and from the measurements it makes in its environment
BEL(x) = P(x|U,Z)
  U: motions (odometry)
  Z: measurements (landmarks, distances)

## Slide 39: Bayes filter
Motion model: P(xt|ut, xt-1)
  Probability of x given previous x and motion u
Measurement model: P(zt|xt)
  Probability of measuring z when in position x
zt
xt
xt
xt-1
ut

## Slide 40: Bayes filter
Prediction using motion model
Correction using measurement model
BEL(x)
Prediction
Correction
Bel(x)
motion action: u
measurement: z
Bel’(x)
Increases uncertainty
Decreases uncertainty

## Slide 41: Particle filter
A Bayes filter
Represent PDF’s by discrete particles (samples)
Each particle is a hypothesis

## Slide 42
Monte Carlo Localization (MCL)

## Slide 43: AMCL
Adaptive Monte Carlo Localization
http://wiki.ros.org/amcl
/scan
AMCL
/particlecloud
/tf
/amcl_pose
map → odom
map
rviz
map_server

## Slide 44: AMCL visualization in RVIZ

## Slide 45: What if we do not have a map?
Let the robot make one
  Drive it around to learn
    Random walk
    Teleoperated
Problem
  To make a map we need the robots location
  But…to localize we need a map

## Slide 46: SLAM
Simultaneous Localization and Mapping
Bayes filter
  Each particle represents a possible map
  Survival of the fittest

## Slide 47: GMAPPING
SLAM
http://www.ros.org/wiki/gmapping
/scan
slam_ gmapping
/map_metadata
/tf
/map
map → odom
map_saver

## Slide 48: Navigation
Given the map and a goal…we need a plan to get to the goal, while avoiding obstacles!

## Slide 49: Path Planning
robot
goal

## Slide 50: Problem
Robot is not a “point in space”
  Has footprint

## Slide 51: Configuration space
“inflation”

## Slide 52: Discretization

## Slide 53: Problems
New and removed obstacles
  Humans
  Furniture

## Slide 54: costmap
Stores information about obstacles
Inputs
  Sensors (dynamic: laserscan, pointcloud)
  Map (static)
Inflates obstacles
  To avoid contact with robot
http://www.ros.org/wiki/costmap_2d

## Slide 55: ROS Navigation stack
local_planner
global_planner
Path
goal
/cmd_vel
global_costmap
local_costmap
map
/scan
move_base
odom/tf

## Slide 56: global_planner
Uses global costmap derived from Map
Computes long-term, global plan
  Optimistical, i.e. unaware of new obstacles and of robot’s actual footprint and dynamics (speed/acceleration limitations )
Algorithm
  Shortest path
    Dijkstra (default)

## Slide 57: local_planner
Uses local costmap, updated by obstacle sensors
Controller
  Computes a short-term, local plan
  Stays close to path, but avoids obstacles dynamically
  Adheres to dynamics of the robot (min/max speed , acceleration)
  Sends velocity commands to the mobile base of the robot
Algorithms
  Trajectory scoring
    DWA, Trajectory rollout

## Slide 58: DWA local planner
Dynamic Window Approach
  Predict (simulate) outcome of sample velocities
  Score each and pick the highest-scoring